## Slide 1: Popularity-Based Prefetching for Video Streaming in Named Data Networking
By Henrik Buhl
Supervisor: Rune Hylsberg Jacobsen

## Slide 2: Agenda
Introduction
Background
  TCP/IP
  NDN
Implementation
  NDN-simulation
  Data extraction
Testing and Results
Conclusion

## Slide 3: Introduction - motivation
Motivation:
The TCP/IP architecture struggles with high latency and bandwidth waste in video streaming. Named Data Networking (NDN) addresses these issues with in-network caching, improving data retrieval and reducing congestion. However, traditional prefetching fails to account for dynamic user behavior, leading to inefficient caching and bandwidth usage.

## Slide 4: Introduction – Purpose and goals
Purpose:
“Explore how user engagement data specifically information about which segments of a video are frequently viewed or skipped can inform more intelligent prefetching strategies in NDN.”
Goals:
Identify segments of content that are frequently accessed or skipped.
Prefetch and cache popular segments closer to the user to reduce latency.
Minimize unnecessary data transfers and improve overall QoE.

## Slide 5: Background – TCP/IP
TCP Handshake
Get request
Fragments
Routing
MAC and Checksum

## Slide 6: Background – TCP/IP HAS
Source: https://teyuto.com/blog/what-is-mpeg-dash-history-pros-and-cons-of-dash
Notes: Video Preparation: The server encodes the video into multiple bitrates, segments it, and generates a manifest file.
Client Initialization: The client downloads the manifest file and begins playback by fetching the first segment.
Dynamic Adaptation: The client monitors network conditions and adjusts the bitrate of subsequent segments dynamically.
Segment Requests: The client requests segments one at a time, ensuring efficient use of bandwidth.
Playback: The client buffers and plays the video, adapting to network changes seamlessly.

## Slide 7: Background – NDN
NDN Forwarding and caching.
Notes: A consumer sends an Interest packet for data through a router.
The router checks its Content Store:
  Hit: The data is retrieved
  Miss: The router checks the PIT.
If the PIT has a matching entry, then the request is aggregated under existing entries.
If the PIT misses, then the FIB checks for a valid route:
  No route: A NACK is sent back.
  Route found: the interest is forwarded upstream.
As data travels, downstream forwarders may cache the data based on the placement policy.

## Slide 8: Background – NDN policies
Placement policies
LCE, LCD, MCD
Replacement policies
LRU, LFU, FIFO
Source: https://www.ipxo.com/blog/network-routing/

## Slide 9: Implementation – NDN-sim Topology

## Slide 10: Implementation – NDN-sim Scenarios
Scenario 1: Simulate CDN like behaviour as it is being used today. Using NDNsim I disabled caching and the placement and replacement policies. Scenario 2: Simulate NDN with standard caching mechanisms, such as LCE and LRU. Scenario 3: Simulate NDN without standard caching mechanisms, but with popularity-based prefetching. Scenario 4: Simulate NDN with standard caching mechanisms and with popularity-based prefetching.

## Slide 11: Implementation – NDN-sim “Users”
Sequential Behaviour: From start to finish
Skipper Behaviour: From start to finish skipping every other segment
Popular-Only Behaviour: Only wants the most popular segments
Random Behaviour: Requests all segments in a random order
Notes: Husk at det er måske ikke super akademisk, men det er en simulation da der kun er 4 consumers og der kommer alt for meget data I forvejen

## Slide 12: Implementation – Simulation showcase

## Slide 13: Implementation – Data extraction
The script made for data extraction works like so:
It retrieves stored SVG heatmaps from the video using web scraping.
The SVGs are converted to PNG format, allowing pixel-level data analysis.
Engagement data is extracted from the PNGs and saved in a CSV file.
This data is then used to identify popular video segments and recreate graphs that align with the original heatmaps.

## Slide 14: Implementation – Data extraction
The picture to the right is an example of how the data is transformed such that it can later be used for the NDN-simulation.
To get the PNG’s to have the right size we use the following formula:
Where SW is Segment Width, SD is Segment Duration, TVD is Total Video Duration and BW is Base Width.

## Slide 15: Implementation – Extraction showcase

## Slide 16: Metrics and results
Metric | Scenario 1 | Scenario 2 | Scenario 3 | Scenario 4
Delays (µs) | 622 - 622 | 2400 - 2400 | 1725 - 1798 | 1059 - 1059
Hop Counts | 1.0 - 1.0 | 3.0 - 3.0 | 2.0 - 2.0 | 2.0 - 2.0
Retransmissions | 5312 - 5312 | 399 - 400 | 5246 - 5312 | 5246 - 5312
Cache Hit Ratio | N/A | 24.56% - 24.56% | 21.52% - 24.08% | 21.69% - 24.08%
Notes: Delays skal vægtes højst

## Slide 17: Conclusion
Goals:
Identify segments of content that are frequently accessed or skipped. ✅
Prefetch and cache popular segments closer to the user to reduce latency. ✅
Minimize unnecessary data transfers and improve overall QoE. ✅ Kind of …

## Slide 19: The real king of streaming
“YouTube made up 9.7% of all viewership on connected and traditional TVs in the U.S. in May”
Source: https://www.cnbc.com/2024/06/26/youtube-streaming-dominance-media-strategy.html
“YouTube primarily uses TCP for its video streaming service. TCP's reliability and error-checking mechanisms align with YouTube's goal of delivering high-quality video content without loss or corruption.”
Source: https://www.gumlet.com/learn/tcp-vs-udp/
Source: https://www.similarweb.com/website/youtube.com/vs/netflix.com/#ranking
“As of November 2024, the most visited website in the world is Google. The next most popular websites are YouTube, Facebook, Wikipedia, and Instagram.”
Source: https://explodingtopics.com/blog/most-visited-websites